## Slide 1
ML-Based Calibration set for FTIR Backward Compatibility
2/8/2025

## Slide 2
Agenda
1) Introduction
2) Problem Statement
3) Project objective
4) Scope of work
5) Challenges & Limitations

## Slide 3
  Spectroscopy
  Absorbance Technique
  NIR Spectrum
  Spectrometer FTIR
Introduction

## Slide 4
Spectroscopy
the study of the interaction between (EMR) and matter
Near-IR region
W.L = 0.78 – 2.5 µm
Molecules for powder ingredients with uniform wavelength and homogeneous mixture
Absorption
Transmission
Reflection
Scattering
W.N = 4000 – 12800 cm⁻¹

## Slide 5
Absorbance Technique
Chemical analyzers use Beer–Lambert’s law
The amount of light absorbed by a substance is proportional to:
  Concentration of the substance
  Length of the light path (path length)
A=log10​(1/T)

## Slide 6
NIR Spectrum
  Matters --> molecules linked by chemical bonds, and these bonds are in a constant state of vibration.
Absorption Conditions (Functional Group):
  The bond must contain hydrogen (such as C–H, O–H).
  The bond must be asymmetric.
  The energy (or frequency) we drop must be close to the natural vibrational energy of the bond.
Wave number
Peak
Transmission %
motion between atoms

## Slide 7
FTIR Spectrometer
Components:
  Infrared source
  Interferometer
  Sample holder
  Detector
  Fourier Transform software
Why used:
  Fast (quick)
  Does not damage the sample (non-destructive)
  Accurate in analyzing chemical bonds
  Works on a variety of conditions.
It does not measure frequencies directly; it measures the superposition of signals. Fourier Transform

## Slide 8
Problem Statement
  Modern FTIR spectrometers, especially newer or miniaturized models, may produce spectra that differ from older hardware versions.
  These spectral differences create incompatibility across devices.
  This leads to increased calibration costs, time, and complexity when upgrading or deploying multiple spectrometers.

## Slide 9
Project Objectives
Build ML model (e.g., PLS regression) to predict the concentration of target materials from the spectra.
  Evaluate backward compatibility by measuring prediction bias across spectrometers.
  Fabricate a calibration set consisting of powdered material mixtures (e.g., starch, protein, salt, vitamin C)

## Slide 10
Project Objectives

## Slide 11
  LHS of Calibration Sets
  Spectral Data Acquisition HW
  Preprocessing, Modeling
  Evaluation, PCA
Methodology

## Slide 12
LHS
LHS (Latin Hypercube Sampling) is:
  A statistical sampling method used to efficiently generate combinations of variables that cover the full range of each variable with minimal redundancy.
  gives a well-distributed set of mixtures with fewer samples and lower correlation between variables.
  Latin Hypercube Sampling (LHS) within the range of 0–10 grams for each of the 20 samples.
  Each is the concentration value for each ingredient (Y label)

## Slide 13
Correlation
  Achieved an average inter-variable correlation of approximately 0.29
  Converted grammatic values into percentages

## Slide 14
Normalization

## Slide 15
Data Acquisition
Weighed each sample using the sensitive balancing, preserving two decimal floating points.

## Slide 16
Scope of work
Sealed each sample in plastic bags to ensure homogeneity then glass holders.

## Slide 17
Scope of work
Applied each sample to the reference spectrometer to obtain spectral data (X label)

## Slide 18
Scope of work
Built Partial least squares (PLS) regression model on a chemometrics software named SOLO.

## Slide 19
Scope of work
Results for Model R2 Cross Validation score:
  Starch : 0.62
  Protein: 0.74
  Vitamin C : 0.17
  Na₂SO₄ (Salt) : 0.23
After the initial trial resulted in suboptimal model performance due to multicollinearity.
a second experimental setup was designed to overcome previous issues.

## Slide 20
Scope of work
Achieved an average inter-variable correlation of approximately 0.0217

## Slide 21
Scope of work
Built Partial least squares (PLS) machine learning model based on the obtained X and Y labels

## Slide 22
Results
Results for Model R2 Cross Validation score:
  Starch : 0.92
  Protein: 0.86
  Vitamin C : 0.91
  Na₂SO₄ (Salt) : 0.75
Model Improvement Factors:
  Generated new samples without mass constraints.
  Increased dataset size to 60 using oversampling.
  Applied proper preprocessing

## Slide 23
Results
PCA was applied to the full set of spectral data (20 spectra per device) to investigate hardware-induced variability (Backward compatibilty)

## Slide 24
Challenges & Limitations
  Relative small amount of spectrometers that were used
  Each ingredient has different compostion
  The dealing with sensitve balance
  the company`s ownership for the devices

## Slide 25
Thank you
Salma Bassem
Rowaina Reda
Prepared by